## Slide 1: Introduction to Network, Multimedia, Application Scenario & Design
蔡子傑

## Slide 2: 網路科技概論
What is “network”?
  Computer network
  Communication network
Why “networking”?
How “networking”?

## Slide 3
Communication Network
vs.
TCP/IP Internet

## Slide 4: Communication Protocols
Protocol: a standard set of rules for communicating
Standards evolve over time
International agreements make Internet possible
Internet Society makes standards and promotes researchwww.isoc.org
Protocol hierarchy/protocol stack, TCP/IP
  Layers of protocols
  Physical transmission to end application rules and standards

## Slide 7
IP data packet
VERS: IP version number
HLEN: header length
Type of service (TOS)
Total length
Identification: a unique number assigned to a datagram fragment
Flags: fragmented or not
Frag offset
TTL: time to live
Protocol: layer-4 protocol, e.g. UDP, TCP, ICMP, IGRP
Header checksum
IP options
Padding

## Slide 8
Network layer provides an unreliable service (i.e. only best-effort delivery)
  No guarantees about packet loss, data corruption, out-of-order packet arrival, duplicate arrival.

## Slide 9
Diversity of multimedia data signals

## Slide 10
Text
  Unformatted plain text
  Formatted text, such as mathematical expressions, hypertext
  inherently digital
Visual
  Drawing, maps, images, animation, etc
  can be analog and converted into digital
Sound
  Voice, audio, music, etc.
  can be analog and converted into digital

## Slide 11
Multimedia classification from network perspective
Real-Time (RT)
  Bounds on the end-to-end packet delay/jitter
  Further classified as
    Discrete media (DM): discrete quantum as a file or message, e.g.
      MSN/Yahoo messengers (error-intolerant)
      Instant messaging services like stock quote updates (error-tolerant)
    Continuous media (CM): continuously as a stream of messages ,
      Further classified as
        Delay tolerant: Internet webcast
        Delay intolerant: audio, video streaming in conferencing systems
Non Real-Time (NRT)
  Do not have strict delay constraints
  E.g. text and image files

## Slide 12
Network oriented classification of Media Types

## Slide 13
Text
Most popular
Transfer protocols
  ftp, http, SMTP(Simple Mail Transfer Protocol)
Represented in binary as
  7-bit ASCII
  8-bit ISO-8859
  16-bit Unicode
  32-bit ISO 10646

## Slide 14
Error depend on applications
  Loss/error free, use TCP for transport
    E.g. File transfer
  Error-tolerant, can use UDP for transport
    E.g. Instant messaging
Applications that use text as primary media do not have any real-time constraints
  Elastic applications
  E.g. web browsing
However, applications like instant messaging do require some guarantees on experienced delay

## Slide 15
Bandwidth vs. compression scheme

## Slide 16
Audio
Sound/speech converted into digital form using sampling and quantization
Digitized audio media is transmitted as a stream of discrete packets over the network

## Slide 17
Bandwidth vs compression

## Slide 18
Audio loss and delay
Loose requirement on packet loss/errors (or error-tolerant)
  1 to 2% packet loss/error without much degradation
Strict real-time requirement
  Highly interactive and shorter response time
  Bounds on end-to-end delay/jitter to be of acceptable quality, e.g. limited to ~200ms.
  Real-Time Intolerant (RTI) applications, e.g. Internet-Telephony
Weaker bounds on delay/jitter
  Real-Time Tolerant (RTT) application
  Involves one-way communication, relatively low interactivity, e.g. Internet webcast, streaming audio

## Slide 19
Graphics and Animation
Static media like digital images, and dynamic media like flash presentations
An uncompressed, digitally encoded image consists of
  Array of pixels, with each pixel encoded in bits to represent luminance and color
  Tend to be large in size
    E.g. 480x640 pixels and color resolution of 24 bits, requires ~1MBytes.
Compression utilizes spatial redundancy

## Slide 20
Graphics and Animation
Static media like digital images, and dynamic media like flash presentations
An uncompressed, digitally encoded image consists of
  Array of pixels, with each pixel encoded in bits to represent luminance and color
  Tend to be large in size
    E.g. 480x640 pixels and color resolution of 24 bits, requires ~1MBytes.
Compression utilizes spatial redundancy

## Slide 21
Graphics and Animation
Static media like digital images, and dynamic media like flash presentations
An uncompressed, digitally encoded image consists of
  Array of pixels, with each pixel encoded in bits to represent luminance and color
  Tend to be large in size
    E.g. 480x640 pixels and color resolution of 24 bits, requires ~1MBytes.
Compression utilizes spatial redundancy

## Slide 22
Image loss and delay
Images are error-tolerant and can sustain packet loss
  Provided the application used to render them knows how to handle lost packets
Like text file, Do not have any real-time constraints

## Slide 23
Image loss and delay
Images are error-tolerant and can sustain packet loss
  Provided the application used to render them knows how to handle lost packets
Like text file, Do not have any real-time constraints

## Slide 24
Bandwidth vs compression

## Slide 25
Video loss and delay
Error- and real-time requirements are similar to audio media type.

## Slide 26: Multimedia classification from network perspective
Real-Time (RT)
  Bounds on the end-to-end packet delay/jitter
  Further classified as
    Discrete media (DM): discrete quantum as a file or message, e.g.
      MSN/Yahoo messengers (error-intolerant)
      Instant messaging services like stock quote updates (error-tolerant)
    Continuous media (CM): continuously as a stream of messages ,
      Further classified as
        Delay tolerant: Internet webcast
        Delay intolerant: audio, video streaming in conferencing systems
Non Real-Time (NRT)
  Do not have strict delay constraints
  E.g. text and image files

## Slide 27: Network oriented classification of Media Types

## Slide 28: Multimedia expectations from a communication network
Traffic requirement
  Real-time characteristics
    Audio and video must be played back continuously at the rate at which they are sampled
  High bandwidth
    Congestion control
    See table 5, bandwidth requirement
    Compressed media still requires significantly high bandwidth
    Lossy (introduce distortion) and lossless compression
  error

## Slide 29
Error control on networking
Error detection followed by Automatic Retransmission reQuest (ARQ)
  Used by TCP (Transport Control Protocol)
    Provide reliable connection-oriented service
Forward Error Correction (FEC)
  Provide sufficient redundancy to correct errors without retransmission
  May be used by UDP (User Datagram Protocol), because UDP provides connectionless un-reliable service
  Applications that exchange error-tolerant media types (both RT and NRT) typically use UDP for eliminating time lost in retransmissions.

## Slide 30: Internet 與物聯網
Computer Network vs Internet
Internet of “Things”
  輸入 (sensor)
  計算
  輸出、通訊
  Applications? Data where (cloud)? Computing where (cloud)?

## Slide 31: IoT Applications
Smart Home
Vehicular Network
Body Area Network

## Slide 32
DLNA (Digital Living Network Alliance)
A digital home

## Slide 33: Wire to wireless

## Slide 34: Wireless technologies

## Slide 35: Basic Home Use Cases

## Slide 36: Basic Home Use Cases

## Slide 37: Telematics: infotainment in automobiles
Information and entertainment
  Navigation
  Traffic status
  Hand-free communcation
  Location-aware services
  Back-seat infotainment, multimedia entertainment and gaming
  Internet browsing, email access

## Slide 39
Vehicular Networking

## Slide 40
Vehicular application classification
Mobile data gathering
  Vehicle can sense events (image from street or presence of toxic chemicals), process sensed data (recognize license plate), and route to other vehicles
Consumer of content
  Location-aware information, entertainment (movies, music, ads)
Both producers and consumers of content
  Report on road conditions, traffic congestion monitoring, emergency alert

## Slide 41
MobEyes: proactive urban monitoring services

## Slide 42
Spawn: content distribution

## Slide 43
Emergency location-aware live video streaming

## Slide 44
Fleanet: a virtual market place

## Slide 45
Vehicular: Interactive applications
RoadSpeak: Voice Chatting in Vehicular Social Networks
Online “Passenger” Games

## Slide 46
台北市公車站系統

## Slide 47
遠端互動藝術
弄偶者、表演者或虛擬人─ 在無線網路空間內的感觀差異時間:
  保羅‧瑟曼喜歡探索在遠端網絡的世界，並與遠端參與者在網域間互動。
  他透過色彩的調和以及視訊會議技術的運用，讓兩個空間內的參與觀眾，同時被連結在一個虛擬的空間中，變成一個可以互動的視覺裝置作品。
  藉由遠端視訊空間，以及觀者與表演者間親密的接觸，傳達自我反射的裝置作品。

## Slide 48
無線Ad hoc網路在群體異地互動應用
http://www.youtube.com/watch?v=Cwp5EY_AZIo

## Slide 59
How to design & innovation
Design issues?

## Slide 60
Design issues
Client device
  Small/large, mobile/fixed
Network platform
  Broadband, mobile/fixed, always connected
Users
  Service or application needs
Others?

## Slide 61
Figure 10.6: An example of use case diagram
Use case diagrams
A use-case diagram gives the user’s view of a system: it shows how users communicate with the system. A use-case diagram uses four components: system, use cases, actors and relationships. A system, shown by a rectangle, performs a function.

## Slide 62
Figure 10.4: An example of a data flow diagram
Data flow diagrams
Data flow diagrams show the movement of data in the system.

## Slide 63
innovation
Do you have any idea for any “innovation” of application scenario?
What is your thinking about this?

## Slide 64
innovation
What is a good innovation?
What is the flow of innovation?
“executable” is important?

## Slide 65: More applications?

## Slide 67
多媒體網路概論 影片

## Slide 68: Discussion
你可以找一個或設計一個物聯網的情境嗎？並說明這個情境，需要收集怎樣的資料？這些資料是透過何種通訊管道收集的？資料又可能會怎麼處理？以及處理完後會有那些回饋或反應？

## Slide 69: 穿戴科技
What to wear?
  Sensor? Sensing what? (bio, health, motion…)
  Vision? VR or AR or others
  Audio? Music or others
Networking?
  Multi-players?
Application domain?
  Game, education, performance, exercise, health…